## Slide 1: Module 3.3 – Computer Vision
Image Moments

## Slide 2: Image Moments
Image Moments are used to describe the size, orientation, and other properties of an object
The example below has the ball segmented from the rest of the image
Notes: Once a shape has been extracted from an image, it is useful to have values that can characterize the shape, size, or orientation of the object
Moments are single values that can be compute from an extracted shape or outline of a shape.
The initial shape can be obtained using some detection process along with thresholding.

## Slide 3: Computing Area
Assume that I(x,y) is a binary image representing the segmented ball in the previous slide
The area of the ball is:
In a binary image, since each pixel is 1, this sums to the area of the shape
  This is also called the zeroth order spatial moment
Notes: The first set of moments are the spatial moments. These moments are computed without regard to the overall position of the shape in the image.
Suppose that there is a binary image I(x,y) where each pixel in the shape is set to 1 and all other values are set to 0.
You could compute the overall area of the shape by iterating over all the shape pixels and adding them up.
This is called M00 or the zeroth order spatial moment of the shape.
It describes the overall area of the shape.

## Slide 4: Computing the Centroid
The centroid represents the center of mass of the shape
The two first order spatial moments are expressed as:
The x coordinate of the centroid can be computed with:
The y coordinate of the centroid can be computed with:
Notes: Once you have the area of the shape (the zeroth order moment), you can compute the center of mass of the shape.
M10 is the summation of all the x-coordinates of all the pixels in the shape.
If you divide M10 by the area, which is the total number of pixels in the shape, you then obtain the average x-coordinate of the shape.
This is the x-coordinate of the center of mass.
Go through the same process for the y-coordinate.
X bar and Y bar are now the x and y coordinates for the center of mass of the shape.

## Slide 5: Second Order Moments
The second order spatial moments are expressed as:
Notes: The second order spatial moments are shown in this slide
There are 3 second order moments: M20, M11, and M02
These moments can be used in characterizing the orientation of an object, but will not be discussed here.

## Slide 6: Central Moments
Central moments are computed relative to the centroid and are invariant of translation
OpenCV has 2 functions that can generate central moments
  cvGetCentralMoment()
  cvGetNormalizedCentralMoment()
    these moments are normalized to the area and become scale invariant
Notes: The spatial moments are computed without regard to the center of mass of the shape. That is why they are called spatial.
The central moments are with regard to the center of mass of the shape. This center of mass was computed from the first order spatial moment.
The central moments have the property of being translation invariant. If the shape is moved around (translated) in the image, the central moments for the shape will remain the same.
OpenCV has functions to compute the central moments and the normalized central moments.
The normalized versions are normalized by area and they become scale invariant.

## Slide 7: Hu Moments
Another set of 7 moments described by Hu are invariant to scaling, translation, and rotation
OpenCV has a function that can generate the Hu moments
  Call cvMoments() first
  Then call cvGetHuMoments()
Notes: In 1962, Ming-Kuei Hu came up with 7 moments that are invariant to scaling, translation, and rotation
These moments can be easily computed using OpenCV
You will first need to generate the standard central moments and then you can call cvGetHuMoments() which will compute the Hu moments.

## Slide 8
The GPU Teaching Kit is licensed by NVIDIA and California Polytechnic State University under the Creative Commons Attribution-NonCommercial 4.0 International License.