## Slide 1: Module 5.2 – Dead Reckoning
Calculating Positions

## Slide 2: Basic Kinematics
Basic physics equations are used to update the position of the robot
Sensors are used to compensate for environmental noise
Notes: Sensors are essential to dead-reckoning because it is impossible to perfectly program a realistic physics model that is always accurate
However, dead-reckoning still requires the engineer to specify how the robot can move and how sensors indicate these changes in location
The equation on the slide is a basic update to the location of the robot (x) based on the previous x, the velocity in the last time period, and the acceleration.
The x’s, v’s and a’s can be replaced with vectors to specify the kinematics for a two or three dimensional location.

## Slide 3: Choosing a Timestep
Smaller timesteps can yield more precise estimates
Smaller timesteps also produce noisier readings
Timesteps that are too large may miss important fluctuations
Notes: One of the important aspects of building a dead-reckoning system is to define how often the location is updated.
Instead of choosing an arbitrary time duration, you can iterate over several timesteps and measure the accuracy of the robot’s positioning.
Then you choose the time duration that was the most accurate.
It is also important to take into account the measurement rate of your sensors, since you will be limited by how frequently you receive data.

## Slide 4: Using Accelerometers
Accelerometer readings can be used to estimate velocity
Velocity estimates are then used to estimate displacement
The state of the robot is both the current velocity and the current position
Notes: When using accelerometers it is important to calibrate the sensor to ensure that you are getting the true acceleration
The acceleration values read from your sensor may not be m/s^2, so you will have to convert to the appropriate units
Accelerometer readings are given with respect to the location of the accelerometer.
You will need to adjust these accelerometer readings to compensate for the accelerometer location if it is not in the center of the robot.

## Slide 5: Accelerometer Issues
Velocity estimates from acceleration integration can drift over time
Care must be taken when use accelerometers on slopes to account for gravity
Notes: More rapid updates to the velocity can help mitigate the drift of velocity values
Combining accelerometers with other sensors (like encoders) can provide a more accurate estimate of velocity and position
When a robot is on a slope, the acceleration due to gravity can be measured across both compass axis (x and y) as well as z.
Thus the components of the gravitational acceleration must be subtracted otherwise the velocity could be incorrectly affected.

## Slide 6: Using Gyroscopes
Gyroscopes provide orientation information
Changes in the orientation can be used in conjunction with velocity estimates to update the robot’s position
On slippery ground, gyroscopes can be essential to detecting changes in orientation when encoders are unreliable
Notes: Gyroscopes are used in many dead-reckoning systems because they provide mostly accurate orientation information in many environments.
Gyroscopes are essential for stabilizing and orienting drones and flying robots where since there are no wheel encoders
Gyroscopes and accelerometers can be used in conjunction to refine velocity and orientation estimates that can compensate for sloped ground
A limitation of gyroscopes is that they do not detect linear motion (only angular rotations), so they must be paired with other sensors
Gyroscopes are also known to drift over time, so their estimates can be less accurate as the robot continues to move.

## Slide 7: Using Compasses
Like a gyroscope, a compass measures the robot’s orientation
Gyroscopes typically measures orientation in 3d, while a compass measures orientation in 2d.
Since a compass provides absolute orientation, it’s reliability does not degrade over time.
Notes: Compasses are more reliable over long periods of time than gyroscopes but they are limited to 2d and can be distorted by magnets
Like a gyroscope a compass must be used in conjunction to another sensor that measure linear velocity

## Slide 8: Using Encoders
Encoders measure wheel rotation and are often the easiest way to estimate the robot’s velocity
The size and position of the wheels must be known in order to use encoders for estimating velocity
Notes: Encoders are a common choice for wheeled robots that use dead-reckoning because they are reliable and inexpensive
Care must be taken to detect free-spinning wheels or wheel slippage, which can cause encoder data to not accurately represent velocity
Differential drive robots (robots with two independent drive wheels) can easily use encoders
Bicycle-type robots (front wheels can rotate) require more advanced physics calculations and must incorporate the direction of the front wheel

## Slide 9: Differential Drive
Jet is a differential drive robot
Differential drive is a type of robot that has two motorized wheels
r = 7 cm
sep = 36 cm
Notes: The two motorized wheels in a differential drive robot are independent and are fixed on the sides of the robot
The wheels can only spin, their orientation cannot change
Many small mobile robots are differential drive because the kinematics equations are simple and there is no need for an additional directional motor
The dimensions of the diagram are the real dimensions of Jet
In order to balance, most differential drive robots have a caster wheel that is non-motorized and spins freely

## Slide 10: Differential Drive Equations
r is the radius of wheels
ul is the angular velocity of the left wheel
ur is the angular velocity of the right wheel
L is the separation of the wheels
Notes: In lab these equations will be used to update the location of the robot as well as its orientation
Notice that theta is positive when the robot is turning left and negative when the robot is turning right.
It is not necessary for theta to be confined to values between pi and negative pi.
You can quickly check the validity of the equations when the robot is going straight forward or 90 degrees to the left
When the robot goes straight forward, theta is zero, and thus cos(theta) = 1 and sin(theta) = 0 so the robot is only changing its x position
When the robot is going directly left, theta is pi/2, and thus cos(theta) = 0 and sin(theta) = 1 so the robot is only changing its y position

## Slide 11
The GPU Teaching Kit is licensed by NVIDIA and California Polytechnic State University under the Creative Commons Attribution-NonCommercial 4.0 International License.