## Slide 1: Module 7.2 – Control Systems
PID Control

## Slide 2: PID Control
PID: Proportional-Integral-Derivative
Used to quickly minimize the error in a control system
Relatively simple, yet powerful tool
Updates the system based on the current error, derivative of the error, and integral of the error
Notes: PID controllers are an excellent first choice for many control systems
PID controllers are applied when the system is linear
You must tune the PID controller to converge by providing inputs to the system that minimize the error
The equation at the bottom describes how the system input is related to the error - e(t)

## Slide 3: Proportional
Proportional component is based on the current error only
Example: for thermostats when temperature is below reference, then the error is negative so heat should be applied
Notes: The proportional error is the most intuitive aspect of PID control;
When a system has an error, the inputs should be changed to reduce that error

## Slide 4: Integral
Integral component is based on the total cumulative error
Example: for steering systems the heading will need to account for the entire time that the heading was incorrect
Notes: The integral of the error ensures that the PID controller does not drift far away from the reference as errors accumulate
Even if the there is no current error, the integral component can cause the controller to update the system to mitigate the previous errors

## Slide 5: Derivative
Derivative component is based on the change of the error
Example: for fluid systems, the derivative term accounts for how quickly the error (flow rate) changes
Notes: The derivative term can be used as a sort of predictive value. When the derivative is large, then the error is changing rapidly, so it may be best to slow the input to prevent large oscillations
A good derivative parameter will help smooth the system and ensure faster convergence.

## Slide 6: Setting Parameters
Some control systems employ automatic methods for finding the correct parameters
Other manual techniques like Ziegler-Nichols have been used with good success
Tuning a PID controller takes some patience, but the result is a highly efficient control system.
Notes: Automated parameter estimation techniques use heuristics and searching algorithms to find the best values
When tuning your own PID controllers it can be beneficial to follow the rules of methods like Ziegler-Nichols which have been shown to make the parameter search quicker and more deterministic.

## Slide 7: Limitations of PID
PID should only be used on linear systems
PID is reactive and it does not utilize domain-specific knowledge about the process
Since PID parameters are constant, it cannot adapt to fundamental shifts in the response behavior.
Notes: PID is not necessarily optimal.
Many control systems can take advantage of the specifics of the system and thus they can be tuned more precisely than the the paramters of PID

## Slide 8
The GPU Teaching Kit is licensed by NVIDIA and California Polytechnic State University under the Creative Commons Attribution-NonCommercial 4.0 International License.